## Slide 1: Modern Linux on a 486 PC
By: Yeo Kheng Meng (yeokm1@gmail.com)
http://yeokhengmeng.com/2018/01/make-the-486-great-again/
https://github.com/yeokm1/gentoo-on-486/
SP Digital Tech Talk (22 Feb 2018)
Hackware v3.8 (6 Feb 2018)

## Slide 2: What is the oldest x86 processor that is still supported by a modern Linux kernel?

## Slide 3
http://www.zdnet.com/article/good-bye-386-linux-to-drop-support-for-i386-chips-with-next-major-release/
(13 Dec 2012)

## Slide 4: What is a 386 or 486?

## Slide 5: The 386
Released in 1985
First 32-bit CPU by Intel
12 Mhz to 40 Mhz

## Slide 6: The 486
Released in 1989
First to have 8KiB onboard L1 cache
Variants
  486DX: With Floating Point Unit (FPU)
  486SX: Without FPU
16 MHz to 100 MHz

## Slide 7: First Linux announcement
Hello everybody out there using minix –
I’m doing a (free) operating system (just a hobby, won’t be big and professional like gnu) for 386(486) AT clones.
…
PS. Yes – it’s free of any minix code, and it has a multi-threaded fs. It is NOT portable (uses 386 task switching etc), and it probably never will support anything other than AT-harddisks, as that’s all I have :-(.
Linus (torvalds@kruuna.helsinki.fi)
Organization: University of Helsinki
25 Aug 91 20:57:08 GMT
http://www.thelinuxdaily.com/2010/04/the-first-linux-announcement-from-linus-torvalds/

## Slide 8: Prior Work

## Slide 9
“Come together with fellow developers, engineers and designers to build cool projects with absolutely no value whatsoever. Yes, the more boliao the better.”
(9 December 2017)

## Slide 10: Team 486 at Super Silly Hackathon
Huijing and I
Damn Small Linux + Web Page Hosting + Playing Music

## Slide 11: My ancient PC: IBM PS/1 Consultant 2133 19C (built in 1993)
AMD 5X86 486-clone 133mhz
  Fastest 486 clones ever made
  Similar performance to Pentium 75Mhz
Cirrus Logic VLB CL-GD5424 Graphics 512KiB VRAM
  Max 800 x 600
64MB SIMM-72 RAM
48x IDE CD ROM Drive
Gotek 1.44MB floppy emulator
1993 Price: US$2000 Base + US$1000 upgrades
2017 Price: US$5170 = SG$6820

## Slide 12: Expansion slots
3x Industry Standard Architecture (ISA) slots
  Supports Plug-n-Play (PnP)
2x 32MB SIMM-72 RAM slots

## Slide 13: Expansion cards
Sound Blaster 16 (PnP)
10Mbps 3Com Etherlink III 3c509B
CompactFlash-IDE (CF-IDE)
32GB CF card

## Slide 14: Expansion cards loaded

## Slide 15: Demo
uname –a
ifconfig
ping
alsamixer
mocp
nginx
SSH
Git
Python
Go

## Slide 16: How was this accomplished?

## Slide 17: Use typical Linux distributions?
Ubuntu
Linux Mint
Debian
Arch Linux
Open Suse

## Slide 18
https://lists.debian.org/debian-devel-announce/2016/05/msg00001.html

## Slide 19
“Gentoo Linux is a Linux distribution built using the Portage package management system. Unlike a binary software distribution, the source code is compiled locally according to the user’s preferences and is often optimized for the specific type of computer.”
From https://en.wikipedia.org/wiki/Gentoo_Linux

## Slide 20: Key steps
Prepare compilation laptop
Partition Disks
Set compilation parameters
Configure Linux Kernel
Compile kernel and other programs
Bootloader
Move CF card to ancient PC and hope it works!

## Slide 21: Step 1: Prepare compilation laptop
Intel Core i7-3520M (3.50 GHz, 4MB L3, 1333MHz FSB)
Intel HD Graphics 4000
16GB DDR3 – 1600MHz
Gigabit Ethernet
Ultrabay DVD-RW
USB-CF adapter

## Slide 22: Step 2: Disk partitioning
Boot: 128MiB
  Must be within 504MiB BIOS limit
Swap: 2GiB
Root: 24.4GiB

## Slide 23: Step 3: Set GCC Compilation parameters
/etc/portage/make.conf
CFLAGS="-O2 -march=i486 -pipe"
CHOST="i486-pc-linux-gnu"

## Slide 24: Step 4: Configure Linux kernel
Disable 64-bit kernel
Set lowest supported CPU to 486

## Slide 25: Step 4: Configure Linux kernel
Enable ISA
Enable ISA Plug and Play

## Slide 26: Step 4: Configure Linux kernel
Add 3Com 3c509 driver

## Slide 27: Step 4: Configure Linux kernel
Add Soundblaster 16 driver

## Slide 28: Step 6: Compile kernel and other programs

## Slide 29: Step 6: Install Bootloader
Install LILO
Grub2 causes reboot loop

## Slide 30: Move CF card to ancient PC and pray!

## Slide 31: Problems

## Slide 32: Data corruption with 80-pin PATA cable
Troubleshooting steps I took
Disconnect CD-ROM drive as primary slave
Replace the CF card
Trying different 80-pin conductor cables
Recompiling the Linux kernel many times with different SATA/PATA options
80-pin
40-pin

## Slide 33: Tough Gentoo installation procedure
Install all required packages manually
Compile packages from source
Configure all config files
Easy
Difficult

## Slide 34: Long iteration cycle
Move CF card to compilation PC
Configure/Compile
Move CF card to ancient PC
Watch bootup/Test

## Slide 35: Low Profile Extension (LPX) Power Supply Failed 
/

## Slide 36: Replace with Small Form Factor (SFF) PSU?

## Slide 37: Use 150W PicoPSU + ATX-AT converter

## Slide 39: Conclusion
Linux still supports the 486 as claimed!!!
Dog slow:
  11 minutes to boot
  5.5 minutes to shutdown
  Cannot multi-task well with modern software
Meltdown and Spectre proof!

## Slide 40: Slashdot and Hackaday
https://linux.slashdot.org/story/18/01/07/228222/can-you-install-linux-on-a-1993-pc
https://hackaday.com/2018/01/07/go-retro-to-build-a-spectre-and-meltdown-proof-x86-desktop/

## Slide 41: Questions?
By: Yeo Kheng Meng (yeokm1@gmail.com)
http://yeokhengmeng.com/2018/01/make-the-486-great-again/
https://github.com/yeokm1/gentoo-on-486/